## Slide 1: Interpolation, Integration, and Coordinate Transformations: Continuous Functions Versus Discrete Samples
Robert P. Goddard University of Washington, Seattle
Northwest C++ Users Group 16 May 2018

## Slide 2: Introduction: Model Problem
Simulation of a passive (listen-only) sonar system with moving source and receiver. Trajectories are specified using 12-parameter snapshots. Source signal is specified using digital samples. The output is received sound, as digital samples.
October’s model problem is similar: Camera on airplane reporting location of a vehicle on the ground.

## Slide 3: Section 1: Interpolation

## Slide 4: Over-Sampled Narrow-Band Signal
196 Hz (tenor G)
2-second length
Hann window
10 kHz sampling rate
  25 x Nyquist
Narrow band and short length are conflicting goals.
Smooth envelope reduces sidelobes
Cost: wider main lobe, less energy for given peak

## Slide 5: Normally Sampled Narrow-Band Pulse
Same Pulse
500 Hz sampling rate
  1.25 x Nyquist
Can we recover our original signal from these samples? How? How well?

## Slide 6: Resampled with Order = 0
Same Pulse
500 Hz sampling rate
Resampled to 10 kHz
Nearest neighbor
Discontinuous
Lots of bad sidelobes
Quiz: Why is the FFT real?

## Slide 7: Resampled with Order = 1
Same Pulse
500 Hz sampling rate
Resampled to 10 kHz
Linear Interpolation
Continuous value
Discontinuous derivative
Lots of bad sidelobes

## Slide 8: Resampled with Order = 3
Same Pulse
500 Hz sampling rate
Resampled to 10 kHz
Interpolated using piecewise cubic polynomials
Values and first derivatives are continuous
First sidelobe -9 dB, others below -40

## Slide 9: Resampled with Order = 7
Same Pulse
500 Hz sampling rate
Resampled to 10 kHz
Interpolated using Windowed Sinc
Smooth but still distorted
One sidelobe, -20 dB

## Slide 10: Resampled with Order = 15
Same Pulse
500 Hz sampling rate
Resampled to 10 kHz
Interpolated using Windowed Sinc
Nailed it!
Order rule of thumb:
  2.5/clear_fraction

## Slide 11: Resampled Using FFT
Same Pulse
500 Hz sampling rate
Resampled to 10 kHz
Interpolated using FFT, zero-pad, IFFT
Exact for this signal (except roundoff)
Effective order is full signal length
Sometimes this is optimal! Compare order to log2(N).

## Slide 12: Interpolated Impulse
15
7
3
1
0
Value=1 at t=0
Value=0 at other sample positions
500 Hz sampling rate
Resampled to 10 kHz
Varying order
Interpolated curve is a sum of these, each centered on and scaled by an input sample

## Slide 13: Interpolation as Linear Transformation
The interpolation algorithms we have seen so far are linear transformations.
Each output value is a weighted sum of input values.
Interpolation is multiplication by a band matrix: Width of central band is order + 1:
where the weights are nonzero only for sufficiently small
  Other forms do not have that property.
  Rational functions, for example, can have better properties for extrapolation.
  But we will ignore such forms.

## Slide 14: Interpolation With Derivatives
If we start out knowing one or more derivatives at our sample points, we can use them similarly:
And so forth for higher derivatives.
Two function values and two first derivatives, at the ends of some interval, define a cubic polynomial in that interval.

## Slide 15: Cubic Weights With Derivative
Each plot shows how one input sample (x or x’) influences a range of output values (y or y’), from that sample’s left neighbor to its right neighbor.

## Slide 16: Section 2: Trajectories

## Slide 17: Scenario Sketch
Source
Receiver:
Delay

## Slide 18: Specifying a Trajectory
A Trajectory is a list of Snapshots:
/// Full Constructor Snapshot( double time, ///< Time at which snapshot occurs in trajectory [sec] const Vector& pos, ///< Position [m] const Vector& vel, ///< Velocity [m/s] const Orientation& orient, ///< Heading, Pitch, Roll [deg] const Orientation& oRate ///< Time derivatives of orient [deg/s] );
Its main function is to transform vectors between Vehicle and Earth coordinate systems.
Vectors to transform: Sensor locations and orientations, sound propagation directions, scatterer locations and velocities, etc.

## Slide 19: Transforming a Vector
  : A location in the Earth coordinate system
  ’: The same location in the Platform coordinate system
  : The location of the Platform in the Earth coordinate system
  : A rotation operator taking a vector from Earth to Platform coordinates
The relationship is a linear transformation:
  : transformTo
  : transformFrom
Where is orthogonal: Its transpose is its inverse:
  (unit matrix)

## Slide 20: Rotation Inputs
Class Orientation: {heading, pitch, roll}
  : Heading: Rotation about the Z axis. Range: -180 to 180 degrees
  : Pitch: Rotation about the Y’ axis. Range: -90 to 90 degrees
  Roll: Rotation about the X” axis. Range: -180 to 180 degrees
Demonstrate with tripod
Nearly every operation requires sines and cosines:
A 3D rotation about an axis reduces to a 2D rotation in the plane of the other two axes

## Slide 21: Rotation Matrix from Orientation
Successive rotations = matrix multiplication
= : transformTo again
  : Associative
Notice that is applied to the vector first, and appears on the right in the matrix multiplication:
Naïve multiplication counts (sub-expression elimination can lower them slightly):
  Computing : 15 multiplications (11 with SEE).
  transformTo: 9 multiplications (one matrix-vector multiplication)
  transformTo stepwise sparse: 3*4=12 multiplications (less with some zero angles)
Do this if you have many vectors to transform between the same 2 coordinate systems.

## Slide 22: Problem: Smooth Motion
Try to keep an airplane centered in camera image as it passes overhead.
  Demonstrate with tripod. Roll doesn’t help.
  With HPR rotations, it can’t be done continuously!
  The problem occurs at the axis of the first rotation (heading).
Theorem: For every 3D rotation, there exists an axis such that vectors parallel to that axis are invariant under that rotation.
Proposed representation #3: Unit vector (axis) in the invariant direction, multiplied by a scalar giving the angle of rotation about that vector.
Advantage: Smooth rotation (interpolation) can be done by smoothly varying the angle (magnitude of vector) while keeping the axis constant.
New problem: Find that vector, given orientation (#1) or matrix (#2).

## Slide 23: Quaternions
Abstract definition: A quaternion is a set of 4 real numbers with two operations, addition and multiplication:
  + = [ ]
  Where are unit vectors, analogous to the used in complex numbers
    = = = -1
  Quaternion addition works like vectors: Just add the components.
  Quaternion multiplication:
    +
    - - - + - - +

## Slide 24: Quaternion Subspaces and Properties
Quaternions of the form are isomorphic to the real numbers.
Quaternions of the form are isomorphic to the complex numbers.
Traceless Quaternions, of the form , are isomorphic to 3D vectors.
Unit Quaternions, in which , are isomorphic to the 3D rotation group. I call them Spinors. Also called Cayley-Klein parameters.
Quaternions as a whole form a division ring: a vector algebra in which every element has a multiplicative inverse except the one in which all elements are zero.
Multiplication is associative (i.e. ) and it distributes over addition (i.e. ) but non-commutative (i.e. ).

## Slide 25: Quaternion Coordinate Transformation
  transformTo:
  transformFrom:
  Where quaternions , , and are the vectors , , and in quaternion form (traceless), is a unit quaternion representing the same rotation as matrix , and is its conjugate, defined as
  where
  Cost: 24 multiplications
  Do this only if you have only one vector to transform using a given rotation – if ever. Otherwise it is faster to convert the unit quaternion to a 3-by-3 rotation matrix and then multiply by the vector.

## Slide 26: Quaternion Scalar-Vector Form
  A useful way to look at a quaternion is as a scalar (the first member) and a vector (the last 3 members):
  In that form, multiplication breaks down into familiar pieces:
    + - +
  Where and are the familiar vector dot and cross products.
  Now here is an important punch line:
    Where is a unit vector. In that case, it turns out that
  i.e. the vector contained within a unit quaternion is invariant under the rotation represented by that quaternion.
  We have found the axis vector we need for interpolation … once we have the quaternion.

## Slide 27: Unit Quaternion from Orientation
/// Compute the Spinor (unit quaternion) corresponding to the given orientation angles. /** Heading, pitch, and roll are right-handed rotations about z, y, and x * respectively, in that order, in radians. */ Spinor spinorFromOrient( Orientation orient ) { double ch = std::cos( 0.5*orient.heading ); double sh = std::sin( 0.5*orient.heading ); double cp = std::cos( 0.5*orient.pitch ); double sp = std::sin( 0.5*orient.pitch ); double cr = std::cos( 0.5*orient.roll ); double sr = std::sin( 0.5*orient.roll ); return Spinor( ch*cp*cr + sh*sp*sr, -ch*sp*sr + sh*cp*cr, ch*sp*cr + sh*cp*sr, ch*cp*sr + sh*sp*cr ); }
Cost: 6 trig functions + 16 multiplications, minus some for common sub-expression elimination.
Conclude: Do this only on input from human-readable form.

## Slide 28: Unit Quaternion to Rotation Matrix
/// Convert a Spinor (unit quaternion) to a 3-by-3 rotation matrix void spinorToMatrix( Spinor spinor, float matrix[3][3] ) { float q0 = spinor.R_component_1(); float q1 = spinor.R_component_2(); float q2 = spinor.R_component_3(); float q3 = spinor.R_component_4(); float p00 = q0*q0; float p01 = q0*q1; float p02 = q0*q2; float p03 = q0*q3; float p11 = q1*q1; float p12 = q1*q2; float p13 = q1*q3; float p22 = q2*q2; float p23 = q2*q3; float p33 = q3*q3;
// Continued from left column: matrix[0][0] = p00 - p11 - p01 - p01; matrix[0][1] = p01 + p01 + p23 + p23; matrix[0][2] = p13 + p13 - p02 - p02; matrix[1][0] = p23 + p23 - p01 - p01; matrix[1][1] = p00 - p11 + p01 + p01; matrix[1][2] = p03 + p12 + p03 + p12; matrix[2][0] = p02 + p02 + p13 + p13; matrix[2][1] = p12 + p12 - p03 - p03; matrix[2][2] = p00 + p11 - p22 - p33; }
Cost: 10 multiplications

## Slide 29: Unit Quaternion to Rotation Vector
/// Convert a Spinor (unit quaternion) to the equivalent rotation vector. /** Return the Vector whose direction is that of the axis of the right-handed * rotation corresponding to the Spinor s, and whose magnitude is the * rotation angle in radians. */ Vector spinorToVector( Spinor s ) { Vector u = Unreal( s ); // Last 3 elements double sinHalfAngle = abs( u ); // 3 mults + sqrt if ( sinHalfAngle < AngleTolerance ) return Vector(); double cosHalfAngle = real( s ); // First element double halfAngle = ( cosHalfAngle >= 0.0 ) // Choose the smaller angle ? std::atan2( sinHalfAngle, cosHalfAngle ); : -std::atan2( sinHalfAngle, -cosHalfAngle ); return (2.0/sinHalfAngle) * u; }
Cost: 1 trig function + 1 square root + 6 multiplications + 1 division

## Slide 30: Unit Quaternion From Rotation Vector
/// Convert a rotation vector to the equivalent Spinor (unit quaternion). /* Return the Spinor corresponding to a right-handed rotation about the * vector x by |x| radians. */ Spinor spinorFromVector( Vector x ) { double angle = abs( x ); if ( angle <= angleTolerance ) return Spinor(); // {1,0,0,0} double factor = std::sin( 0.5*angle ) / angle; return Spinor( std::cos( 0.5*angle ), factor * x[2], factor * x[1], factor * x[0] ); }
Cost: 2 trig functions + 4 multiplications

## Slide 31: Interpolating a Rotation
/// Interpolate linearly between two Rotations /** Set *this to a Rotation that lies along a "minimal" path * between the two given Rotations. * The point along that path is computed using linear interpolation * with the given weight. */ void Rotation::Interpolate( const Rotation& prevRot, ///< Previous Rotation const Rotation& nextRot, ///< Next Rotation double weight ///< Interpolation weight, 0 at prev to 1 at next ) { Spinor fullSpinor = nextRot.spinor_ / prevRot.spinor_; // 4 mult Vector vecFull = spinorToVector( fullSpinor ); // 1 trig + 1 sqrt + 7 mult Vector vecDelta = weight*vecFull; // 3 mult Spinor spinDelta = spinorFromVector( vecDelta ); // 2 trig + 4 mult spinor_ = spinDelta * prevRot.spinor_; // 4 mult }
Simplified for presentation by omitting time derivatives.
Spinor spinor_ is a member of Rotation.
Cost: 3 trig functions + 1 square root+ 22 multiplications
Can be reduced if there are many interpolation points between the same 2 rotations

## Slide 32: Summary: Representations of Rotations
Orientation angles (e.g. heading, pitch, roll)
  Use only for human-readable I/O
  Conversion to other representations require trig functions
  Difficult to compute from the other forms (iterative nonlinear solver)
Matrix (3 by 3, orthogonal, 6 constraints)
  Most efficient for transforming vectors
  Difficult to convert to any other representation
Unit Quaternion (4 reals + 1 constraint)
  Easy to compute compound rotation (multiply)
  Reasonably easy to compute from orientation angles or rotation vector
  Easy to convert to matrix or rotation vector
Rotation Vector (3 reals)
  Required for interpolating rotations (and extrapolating, not shown)
  Reasonably easy to convert to or from unit quaternions
All four are required for an efficient, full-featured 3D geometry library.